## Slide 1: Visitor flow surveilance
A project about Movement monitoring

## Slide 2
Why collect this data?
Staff planning
investment validation
Cleaning services
Resource planning
Notes: Staffplanning: How much staff is needed on this youth recreation center?
Investment validation: Do people actually use this facility, when in the day is it used?
Cleaning service: and garbage handling
Resource planning: On this specific week day usually many people go to this place and then we need this many police in the area.

## Slide 3: Modern applications
Camera stream connected to computer
Ai scans video and counts
Cons:
Cameras are not allowed everywhere
Feeling of always beeing watched
Requires powerful and expensive hardware
Notes: Camera connected to computer: both over network or direct
Camera are not allowed in some areas, requires application for permissions

## Slide 4: AMG8833 IR Thermal Camera
Returns Array with 64 temperatures
”Can detect a human from a distance of up to 7 meters”

## Slide 5: Sence movement
Divided the 64 pixels into two zones
Looks at difference in average temperature
Notes: Looks at diffrence in average temperature between zones and can by that tell in what direction someone is passing the sensor.

## Slide 6: Optimization
By using fewer pixels the zones gets less noice
Notes: From sensors perspective
Right now i am only using the 32 middle pixels because that turned out to give less background noice.

## Slide 7: Optimization
Fine tuning Temperature difference limit
Depends on mounting location
Too low: below 0.4 °C
Too high:
Above 1 °C
Notes: A lower gives easier sensing but are more prone to noise
A too high value will cause the device too miss humans passing.
The perfect value for the two locations i have tried seem to be somewhere between 0.5-0.9 deggrees.
Before optimization was done it triggered easily. Vacuum robot triggered it and on the cloud service it said that it was 42 pople in my small kitchen.

## Slide 8: WiFi traffic scanning
Smartphones with wifi turned on
Scans for wifi nodes
estimates how many people are nearby
Notes: Looks at individual devices by looking at their mac adress.

## Slide 9: Promiscuous mode
1
2
2
1
MAC address: 1
1
2
2
1
MAC address: 1
Non-promiscuous mode (normal)
Notes: Need a device that supports promiscuis mode
CPU can look at packet information and retrive the mac address of the package

## Slide 10: TTL- Time To Live
Inititiation scan adds background traffic to ignore list
New unknown devices gets a ttl of 60 seconds
The timer is reset every time the mac-address is found
If the ttl gets below zero, the address is dropped

## Slide 11: The tasks
Movement monitoring
LED indication
Wifi packet sniffer
Wifi client & mqtt
Priority: High
Core: --
Priority: Low
Core: 0
Priority: Medium
Core: 0
Priority: Medium
Core: 0
Notes: Code is structured into four tasks
FreeRTOSlets you set core and priority
Describe different tasks

## Slide 12: The device
Fitted into connection box
Had to add a button
Higher power consumption than expected
Notes: Battery is no option

## Slide 13: Positive results
Walking in and out ten times
Running in and out five times
Walking in and out with boiler in hand four times
Notes: Looks at individual devices by looking at their mac adress.

## Slide 14: Negative results
Walking in and out five times with hat and jacket
Walking but stopping under sensor for ten seconds then continue (five times)
Notes: Issue with vauum robot

## Slide 15: Wi-Fi result
Reception is too strong
Improvement: add rssi controll
Notes: Pics up packets from people walking and driving by house.
All neighbours devices.